## Slide 1
Evaluating the Effectiveness of IP Hopping via an Address Routing Gateway
Ryan Morehart, 2Lt
AFIT/ENG
21 February 2013

## Slide 2: Acknowledgements
Thesis Committee
  Dr. Barry Mullins – Advisor
  Dr. Rusty Baldwin
  Dr. Timothy Lacey

## Slide 3: Overview
Motivation and Goals
Background
Implementation
Methodology
Results
Conclusions
Future work
Summary

## Slide 4: Overview
Motivation and Goals
Background
Implementation
Methodology
Results
Conclusions
Future work
Summary

## Slide 5: Motivation
Networks are critical to many aspects of the modern military and corporations
  Protecting these is a huge concern
  Traditional network defenses (firewalls, IDS/IPSs) help
Interest in more dynamic protection
  Reputation/trust-based security
  Machine learning
  Network address space randomization (“IP hopping”)

## Slide 6: Goals and Approach
Overall goal:
  Study the effectiveness of IP hopping in classifying traffic
Approach:
  Develop custom IP hopping solution combining previous research to meet military network needs
  Create test network on physical servers
  Test with traffic generators

## Slide 7: Overview
Motivation and Goals
Background
Implementation
Methodology
Results
Conclusions
Future work
Summary

## Slide 8: Background – IP Hopping
Formally part of “network address space randomization”
Involves changing IP addresses periodically
  No distinguishable pattern to outside observer
  “Hops” typically chosen based on a shared secret
  Often coupled with encryption between IP hopping systems

## Slide 9: Background – IP Hopping
Presents a moving target to attacker
  Obfuscates true sender of sniffed traffic
  Network maps established by attacker change frequently
Two basic approaches:
  End point-based
  Gateway-based

## Slide 10: Background – Gateway Hopping
In gateway hopping, a system in front of the network transforms packets

## Slide 11: Overview
Motivation and Goals
Background
Implementation
Methodology
Results
Conclusions
Future work
Summary

## Slide 12: Implementation – Requirements
Security over any network (including confidentiality)
Utilizes existing commercial infrastructure
Must not terminate connections unnecessarily
Easily deployable on existing network
  No hardware changes
  Minimal software configuration changes
  Allow use with legacy systems

## Slide 13: Implementation – Features
Custom solution referred to as the Address Routing Gateway (ARG)
Gateway-based solution
Capable of hopping many times per second
Fully encrypted and authenticated packets between ARG-protected networks
No connection drops across hops
No configuration changes needed on protected hosts
Easy configuration for each gateway
  Self: private key, hop interval, IP range
  Others: public key, IP range
  Each gateway can exchange data to expand each gateway’s gateway list without having configuration files

## Slide 14: Implementation – Architecture
Three components
Director – Receives incoming packets and decides how to handle
Hopper – Maintains gateway information
Network Address Translator – Handles external connections

## Slide 15: Overview
Motivation and Goals
Background
Implementation
Methodology
Results
Conclusions
Future work
Summary

## Slide 16: Methodology – Research Questions
Does ARG classify traffic correctly? What percentage of false positives (valid packets blocked) and false negatives (invalid traffic allowed through) does it introduce?
What is the maximum packet rate and throughput ARG can support?
What is the minimum supportable time between hops? How does latency affect this?
Is ARG stable when presented with corrupt, malformed, or replayed packets?

## Slide 17: Methodology – Research Questions
Does ARG classify traffic correctly? What percentage of false positives (valid packets blocked) and false negatives (invalid traffic allowed through) does it introduce?
What is the maximum packet rate and throughput ARG can support?
What is the minimum supportable time between hops? How does latency affect this?
Is ARG stable when presented with corrupt, malformed, or replayed packets?

## Slide 18: Methodology – Research Questions
Does ARG classify traffic correctly? What percentage of false positives (valid packets blocked) and false negatives (invalid traffic allowed through) does it introduce?
What is the maximum packet rate and throughput ARG can support?
What is the minimum supportable time between hops? How does latency affect this?
Is ARG stable when presented with corrupt, malformed, or replayed packets?

## Slide 19: Methodology – Research Questions
Does ARG classify traffic correctly? What percentage of false positives (valid packets blocked) and false negatives (invalid traffic allowed through) does it introduce?
What is the maximum packet rate and throughput ARG can support?
What is the minimum supportable time between hops? How does latency affect this?
Is ARG stable when presented with corrupt, malformed, or replayed packets?

## Slide 20: Methodology – Test Network
7 physical systems on 4 VLANs
Artificial latency introduced on hosts via tc
Traffic generators used for testing

## Slide 21: Methodology – Metrics
Percentage of invalid packets accepted (false negative)
  “Invalid” traffic should not be allowed in by ARG
Percentage of valid packets rejected (false positive)
  “Valid” traffic should be allowed in by ARG
Types of rejections seen
Kilobits per second of traffic

## Slide 22: Methodology – Factors
Hop interval (ms) – Time between address changes
Round-trip latency (ms) – Artificial latency
Packet delay (s) – Time between sends from the traffic generators
Traffic direction and type – “Traffic flows”

## Slide 23: System Under Test

## Slide 24: Methodology – Traffic Flows
Traffic Flow 0
Traffic Flow 1

## Slide 25: Methodology – Traffic Flows
Traffic Flow 2
Traffic Flow 3

## Slide 26: Methodology – Traffic Flows
Traffic Flow 4
Traffic Flow 5

## Slide 27: Methodology – Traffic Flows
Traffic Flow 6
Traffic Flow 7

## Slide 28: Methodology – Traffic Flows
Traffic Flow 8

## Slide 29: Methodology – Test Sequences
Testing broken into four sequences to focus on each research question:
  Basic tests
  Maximum throughput
  Minimum hop interval
  Fuzz testing

## Slide 30: Methodology – Test Sequences
Basic tests – Validate basic functionality of ARG by exercising every traffic flow
Factor | Possible Levels
Hop Interval (ms) | 500, 50
Round-trip latency (ms) | 20
Packet delay (s) | 0.3
Traffic direction and type | Flows 0-8

## Slide 31: Methodology – Test Sequences
Maximum throughput – Test the maximum traffic rate ARG can handle
Factor | Possible Levels
Hop Interval (ms) | 500, 50
Round-trip latency (ms) | 20
Packet delay (s) | 0.2, 0.1, 0.05, 0.01, 0.005, 0.001
Traffic direction and type | Flow 4

## Slide 32: Methodology – Test Sequences
Minimum hop interval – Test the maximum supportable hop rate with loss below 2%
Factor | Possible Levels
Hop Interval (ms) | 1000, 500, 300, 200, 100, 75, 60, 50, 40, 30, 15, 10, 5
Round-trip latency (ms) | 0, 30, 100, 500
Packet delay (s) | 0.3
Traffic direction and type | Flow 4

## Slide 33: Methodology – Test Sequences
Fuzz testing – Replay traffic with any of several possible modifications
Factor | Possible Levels
Hop Interval (ms) | 500, 50
Round-trip latency (ms) | 20
Packet delay (s) | 0.3
Traffic direction and type | Flow 8

## Slide 34: Overview
Motivation and Goals
Background
Implementation
Methodology
Results
Conclusions
Future work
Summary

## Slide 35: Results – Basic Tests (Valid)
Mean and 95% CI for valid traffic in basic tests.
Overall mean loss of 0.11%

## Slide 36: Results – Basic Tests (Valid)
Basic tests, flows 1-4. Packet rejection reasons. 143 repetitions with 2,312,228 total packets represented.
Reason | Count | % of Total Packets
Outbound message too long | 949 | 0.041%
Outbound sequence number incorrect | 596 | 0.0258%
Inbound unwrapped | 578 | 0.025%
Unknown | 518 | 0.0224%
Outbound gateway not connected | 393 | 0.017%
Inbound NAT bucket not found | 173 | 0.00748%
Inbound gateway not connected | 78 | 0.00337%
Inbound bad protocol | 57 | 0.00247%
Inbound source IP incorrect | 30 | 0.001297%
Inbound destination IP incorrect | 6 | 0.000259%
Inbound ping accepted | 3 | 0.000129%
Lost on wire | 2 | 0.0000865%
Outbound rewrite | 1 | 0.00004325%

## Slide 37: Results – Basic Tests (Invalid)
Basic tests, packet loss of invalid traffic
Flow | Mean | CI | Replications
Flow 5 | 100% | (100%, 100%) | 28
Flow 6 | 100% | (100%, 100%) | 28
Flow 7 | 100% | (100%, 100%) | 28
Flow 8 | 100% | (99.9%, 99.9%) | 28

## Slide 38: Results – Basic Tests (Invalid)
Basic tests, flows 5-8. Packet rejection reasons. 112 repetitions with 1,268,746 total packets represented.
Reason | Count | % of Total Packets
Inbound NAT bucket not found | 60,884 | 4.799%
Inbound unwrapped | 687 | 0.05415%
Outbound message too long | 486 | 0.03831%
Unknown | 340 | 0.0268%
Outbound sequence number incorrect | 242 | 0.01907%
Inbound source IP incorrect | 14 | 0.001103%
Inbound ping accepted | 5 | 0.0003941%

## Slide 39: Results – Minimum Hop Interval
Hop interval tests, packet loss of UDP and TCP traffic between ARG networks

## Slide 40: Results – Minimum Hop Interval
Hop interval test loss reasons. 612 tests with 15,387,651 total packets represented
Reason | Count | % of Total Packets
Inbound destination IP incorrect | 506,075 | 3.289%
Inbound source IP incorrect | 165,656 | 1.077%
Inbound unwrapped | 4,935 | 0.0321%
Unknown | 4,235 | 0.0275%
Outbound message too long | 4,106 | 0.0267%
Outbound sequence number incorrect | 2,180 | 0.0142%
Outbound gateway not connected | 1,000 | 0.006499%
Inbound NAT bucket not found | 110 | 0.0007149%
Inbound bad protocol | 94 | 0.000611%
Inbound gateway not connected | 14 | 0.0000998%
Outbound wrapped | 12 | 0.00007798%

## Slide 41: Results – Maximum Throughput
Packet rate tests, clustered loss verses throughput
Clust | Mean (Kbps) | Min (Kbps) | Max (Kbps)
1 | 485.1 | 300.3 | 573.7
2 | 854.5 | 782 | 980.3
3 | 1401 | 1190 | 1581
4 | 2223 | 1969 | 2421
5 | 3250 | 3243 | 3264
6 | 3796 | 3778 | 3814
7 | 4374 | 4351 | 4389

## Slide 42: Results – Maximum Throughput
Packet rate tests, Tukey test against clustered data
Clust | Mean (Kbps) | Min (Kbps) | Max (Kbps)
1 | 485.1 | 300.3 | 573.7
2 | 854.5 | 782 | 980.3
3 | 1401 | 1190 | 1581
4 | 2223 | 1969 | 2421
5 | 3250 | 3243 | 3264
6 | 3796 | 3778 | 3814
7 | 4374 | 4351 | 4389

## Slide 43: Results – Fuzz Testing
ARG remains stable throughout fuzz testing
21.8% to 23.6% packet loss reported
  Results not validated
  Cause unknown, further examination needed

## Slide 44: Overview
Motivation and Goals
Background
Implementation
Methodology
Results
Conclusions
Future work
Summary

## Slide 45: Conclusions
Does ARG classify traffic correctly?
  Overall, yes
  0.11% of valid traffic is lost on average
  100% of invalid packets are dropped
What is the maximum throughput ARG can support?
What is the minimum supportable time between hops? How does latency affect this?
Is ARG stable when presented with corrupt, malformed, or replayed packets?

## Slide 46: Conclusions
Does ARG classify traffic correctly?
What is the maximum throughput ARG can support?
  Capable of supporting at least 4 Mbps
  No trend indicates this is the upper limit
What is the minimum supportable time between hops? How does latency affect this?
Is ARG stable when presented with corrupt, malformed, or replayed packets?

## Slide 47: Conclusions
Does ARG classify traffic correctly?
What is the maximum throughput ARG can support?
What is the minimum supportable time between hops? How does latency affect this?
  Hop interval must exceed two times the round-trip latency
  50 to 75 milliseconds appears to be a hard lower limit
Is ARG stable when presented with corrupt, malformed, or replayed packets?

## Slide 48: Conclusions
Does ARG classify traffic correctly?
What is the maximum throughput ARG can support?
What is the minimum supportable time between hops? How does latency affect this?
Is ARG stable when presented with corrupt, malformed, or replayed packets?
  ARG remains stable
  May exhibit high packet loss
  More exploration is needed to learn why

## Slide 49: Overview
Motivation and Goals
Background
Implementation
Methodology
Results
Conclusions
Future work
Summary

## Slide 50: Future Work
IPv6 support
Fragmentation support
Latency compensation
  Change hop rate for high-latency connections
  Send with IP addresses “in the future”
More extensive malicious testing
Integration with other defenses
  IDS
  Honeypot

## Slide 51: Summary
Motivation and Goals
Background
Implementation
Methodology
Results
Conclusions
Future work
Summary

## Slide 52: Questions?
?? || /* */

## Slide 54: Lessons Learned
Begin pilot studies earlier!
Discover performance problems with results processing earlier
Better understanding of hop rate-interval interaction and run more fine-grained study
Solve triple-latency issue

## Slide 55: Background - Routing
Hierarchical nature of IP routing allows hopping to work
 | IP | Mask | Interface
1 | 10.5.0.25 | 255.255.0.0 | Port 1
2 | 172.100.10.0 | 255.255.255.0 | Port 2
3 | 172.100.0.0 | 255.255.0.0 | Port 3

## Slide 56: Late Packet Example
Gateway behavior when latency exceeds hop interval

## Slide 57: Results – Minimum Hop Interval
With 5 ms one-way latency on ARP
With latency not affecting ARP

## Slide 58: Incoming Packet Processing
Director packet processing logic

## Slide 59: Incoming Packet Validation
Hopper incoming packet validation

## Slide 60: Fuzzer Modifications
Zero or more modifications chosen
Each modification has 10% probability
Possible modifications:
  Zero ARG signature/HMAC
  Change message type
  Zero data
  Remove the data
  Changed sequence number
  Changed source IP address
  Changed destination IP address